## Slide 1
Liz Willer
15/10/2019
Software Workshop 2:
Lighting Effects Using FastLED

## Slide 2
UNSW Illuminate

## Slide 3
VCC
Data
Ground
The Aly Boards

## Slide 4
Include the library
Make an array
Set up the library
Reduce brightness
Fill the array
Send the data
FastLED.addLeds<WS2811, DATA_PIN, GRB>(leds, NUM_LEDS);
#include <FastLED.h>
FastLED.setBrightness(BRIGHTNESS);
FastLED.show();
FastLED.show();
#includes and global vars
Loop
Setup
The FastLED Library

## Slide 5
RGB
Notes: Image from: https://www.teachengineering.org/makerchallenges/view/spfun_rgbcolor_maker1

## Slide 6: Setting the Colour
More info: https://github.com/FastLED/FastLED/wiki/Controlling-leds
leds[i].r = 255;
leds[i].g = 68;
leds[i].b = 221;
leds[0] = CRGB::Red;
leds[i].setRGB( 255, 68, 221);
leds[i] = 0xFF44DD;
CRGB leds[NUM_LEDS];

## Slide 7
Starter code can be found at:
https://github.com/liz-liz/IlluminateSoftwareWorkshops/blob/master/Blink.ino
Your Task

## Slide 8: Challenge!
You have until 7:45pm to make your prettiest light show
Winner gets a prize